## Slide 1
Software Database: first-week progress
EvolveSWDB 2026-09-24
1
Purpose
Give ArchEvolve a shared record of computation,
memory behavior, and measured performance.
Implemented | Current coverage
Describe and query application code | 6 kernels, 8 implementations
Profile each implementation on each input | 32 profiles across 4 inputs
Screen optimization strategies | 5 strategies, 2 intrinsics
31 profiles complete. Strategy application and measured gains are the next step.
Notes: 0:00–0:45 (45 seconds). ArchEvolve needs a common description of what a kernel computes, how each implementation touches memory, and what profiling measured. We have implemented that Software Database. It keeps these facts in versioned records, supports queries, and exports a workload view for the hardware side. The current application is GAPBS. We have six kernels, eight implementations and thirty-two profiles across four inputs. Thirty-one profiles are complete. This is infrastructure plus initial characterization evidence. The new strategy catalog can screen opportunities, but we have not yet measured an implementation produced by applying one of those strategies. Today I will show one example, the implemented support, and the next experiment I propose.
Sources (repository snapshot a38dfac, reviewed 2026-09-24):
/Users/yanrujhou/CLionProjects/EvolveSWDB/CONTEXT.md
/Users/yanrujhou/CLionProjects/EvolveSWDB/swdb/cli.py
/Users/yanrujhou/CLionProjects/EvolveSWDB/swdb/view.py
/Users/yanrujhou/CLionProjects/EvolveSWDB/.scratch/evolveswdb-2026-09-22/map.md
/Users/yanrujhou/CLionProjects/EvolveSWDB/.scratch/optimization-strategies-2026-09-23/map.md

## Slide 2
One kernel can have different memory behavior
EvolveSWDB 2026-09-24
2
Example: PageRank reads a neighbor’s contribution
contribution[neighbor_index[e]]
Simplified expression: stream through neighbor_index, then read contribution indirectly.
Recorded fact | Gauss–Seidel | Jacobi
Kernel (shared correctness check) | PageRank | PageRank
Access pattern’s update kind | Read | Read
Loop-carried dependency | Yes | No
Code semantics belong to the implementation. Measurements belong to its profiles.
Notes: 0:45–1:45 (60 seconds). A kernel is identified by its computation and correctness check. An implementation is the actual code that passes that check. For PageRank, we record the upstream Gauss-Seidel and Jacobi implementations separately. The example expression is a simplified view of their recorded gather: read a neighbor identifier from an index array, then use it to read a contribution. We represent each array access as a step, so the database retains the indirection rather than only labeling the whole function irregular. Both implementations share this pattern class, but their semantics differ. Gauss-Seidel updates contributions during the sweep and has a recorded loop-carried dependency. Jacobi has a separate contribution pass and no recorded dependency for this gather. A profile then records what happens for one implementation, input and machine. That separation lets us ask useful questions without mixing code facts and measurements.
Sources (repository snapshot a38dfac, reviewed 2026-09-24):
/Users/yanrujhou/CLionProjects/EvolveSWDB/docs/adr/0001-kernel-identity-is-its-correctness-check.md
/Users/yanrujhou/CLionProjects/EvolveSWDB/docs/adr/0003-access-pattern-is-a-chain-of-steps.md
/Users/yanrujhou/CLionProjects/EvolveSWDB/records/implementations/gapbs-pr-gs.yaml
/Users/yanrujhou/CLionProjects/EvolveSWDB/records/implementations/gapbs-pr-jacobi.yaml

## Slide 3
Strategy queries use those code semantics
EvolveSWDB 2026-09-24
3
Packing copies gathered values into a contiguous array
Strategy | Gauss–Seidel | Jacobi
Packing | Illegal | Legal
SIMD gather | Illegal | Legal
Software prefetch | Legal | Legal
“Legal” means encoded conditions pass. Manual checks still remain.
Unknown required facts produce “undetermined.”
Strategy screening and instruction-set checks work. No measured strategy gains yet.
Notes: 1:45–2:45 (60 seconds). The new extension stores reusable optimization strategies separately from executable implementations. Here is a query we can already answer: which strategies satisfy the recorded conditions for this PageRank gather? Packing and SIMD gather are illegal for the Gauss-Seidel record because its loop-carried dependency conflicts with those strategies’ conditions. The Jacobi record passes the encoded conditions. Software prefetch passes for both. These are query results, not proof that changing the program is correct or profitable. The tool also reports undetermined when required facts are unknown. For packing, manual checks still include whether values remain stable between packing and use, and whether reuse pays for the extra pass. We also record intrinsics and derive their required instruction-set extensions, so profiling can reject incompatible machine or compiler settings. No current production record yet declares that it applies these strategies.
Sources (repository snapshot a38dfac, reviewed 2026-09-24):
/Users/yanrujhou/CLionProjects/EvolveSWDB/swdb/strategy.py
/Users/yanrujhou/CLionProjects/EvolveSWDB/swdb/db.py
/Users/yanrujhou/CLionProjects/EvolveSWDB/swdb/isa.py
/Users/yanrujhou/CLionProjects/EvolveSWDB/records/strategies/packing.yaml
/Users/yanrujhou/CLionProjects/EvolveSWDB/records/strategies/simd_gather.yaml
/Users/yanrujhou/CLionProjects/EvolveSWDB/records/strategies/software_prefetch.yaml

## Slide 4
PageRank scaling changes with input size
EvolveSWDB 2026-09-24
4
Jacobi PageRank on mbit10: median of 5 trials per thread count
Chart: Threads
| 1 | 2 | 4 | 8 | 16
Scale 16 (65K vertices) | 1 | 1.99 | 3.87 | 3.95 | 3.93
Scale 22 (4.19M vertices) | 1 | 1.98 | 3.93 | 7.56 | 13.35
At 16 threads
Scale 16: 3.93×
Scale 22: 13.35×
Footprint / socket L3
Scale 16: 0.33×
Scale 22: 23.06×
Same implementation, different scaling. Profiles must retain input and machine context.
Notes: 2:45–4:00 (75 seconds). These are recorded timings for the same Jacobi implementation on two Kronecker inputs. Both runs used the mbit10 Xeon Gold 6326, within one socket, and five trials at each thread count. The chart divides the one-thread median by each multi-thread median. The smaller input reaches about four times speedup and then flattens. The larger input reaches thirteen point three five times at sixteen threads. Their recorded footprints are eight point three three megabytes and five hundred eighty point three five megabytes, compared with a twenty-four mebibyte last-level cache per socket. For the small case, the code’s dynamic chunk size of sixteen thousand three hundred eighty-four gives only four chunks for roughly sixty-five thousand vertices. This helps explain the plateau. We retain measured timing separately from simulated cache misses and inferred bottleneck labels. The result motivates storing profiles per input. It does not by itself establish a memory-latency cause for the larger case.
Sources (repository snapshot a38dfac, reviewed 2026-09-24):
/Users/yanrujhou/CLionProjects/EvolveSWDB/records/profiles/gapbs-pr-jacobi.kron-g16-k16.mbit10.20260922t212416z.yaml
/Users/yanrujhou/CLionProjects/EvolveSWDB/records/profiles/gapbs-pr-jacobi.kron-g22-k16.mbit10.20260922t215412z.yaml
/Users/yanrujhou/CLionProjects/EvolveSWDB/records/machines/mbit10.yaml
/Users/yanrujhou/CLionProjects/EvolveSWDB/apps/gapbs/src/pr_spmv.cc

## Slide 5
Next step: apply and evaluate one strategy
EvolveSWDB 2026-09-24
5
Completed
Records, queries, profiling, workload export, and strategy screening
Current limits
No measured strategy applications. One incomplete correctness check.
All records retain draft status.
Proposed experiment
Choose an eligible strategy and check its remaining conditions.
Implement it, verify correctness, and measure total cost against its baseline.
Advisor discussion: which strategy and implementation should we evaluate first?
Notes: 4:00–5:00 (60 seconds). The completed foundation includes record validation, queries, workload export, profiling, and strategy screening. The current boundary is clear: all records are still drafts, one triangle-counting profile has an incomplete correctness check, and no recorded implementation yet applies a cataloged strategy. I propose making one strategy concrete. We would choose one eligible access pattern, complete the remaining manual checks, implement the change as a derived implementation, and run the kernel’s correctness check. We would then compare that implementation with its own baseline on matched inputs and machine settings, including any added setup work. Packing on Jacobi is a candidate to investigate, not a promised speedup: its amortization may fail. The decision for this meeting is whether this is the right next experiment, and which strategy and implementation should go first.
Sources (repository snapshot a38dfac, reviewed 2026-09-24):
/Users/yanrujhou/CLionProjects/EvolveSWDB/records/strategies/packing.yaml
/Users/yanrujhou/CLionProjects/EvolveSWDB/swdb/strategy.py
/Users/yanrujhou/CLionProjects/EvolveSWDB/swdb/isa.py
/Users/yanrujhou/CLionProjects/EvolveSWDB/schemas/implementation.schema.json
/Users/yanrujhou/CLionProjects/EvolveSWDB/records/profiles/gapbs-tc-ordered.kron-g22-k16.mbit10.20260922t233432z.yaml

## Slide 6
Backup: complete record inventory
EvolveSWDB 2026-09-24 Backup
6
Record kind | Count | What it stores
Application | 1 | GAPBS source and version
Kernel | 6 | Computation and correctness check
Implementation | 8 | Code, loops, and 77 access patterns
Input | 4 | Kronecker / uniform, scales 16 / 22
Machine | 1 | mbit10 hardware and CPU flags
Profile | 32 | Measurements for an implementation/input/machine
Strategy | 5 | Target, effects, conditions, reported benefit
Intrinsic | 2 | Instruction wrapper and required ISA
59 records validate. All are draft. 14 initial tickets and 7 extension tickets are resolved.
Notes: Backup only. Counts are from all YAML records at the stated checkout. The 59 records all retain draft status. Access patterns are nested within implementations, so their count is not added to the record total. All 21 tickets across the initial milestone and strategy extension are marked resolved. Ticket status does not establish research effectiveness.
Sources (repository snapshot a38dfac, reviewed 2026-09-24):
/Users/yanrujhou/CLionProjects/EvolveSWDB/records/
/Users/yanrujhou/CLionProjects/EvolveSWDB/.scratch/evolveswdb-2026-09-22/map.md
/Users/yanrujhou/CLionProjects/EvolveSWDB/.scratch/optimization-strategies-2026-09-23/map.md

## Slide 7
Backup: application and profile coverage
EvolveSWDB 2026-09-24 Backup
7
Kernel | Recorded implementations | Profiles
PageRank | Gauss–Seidel, Jacobi | 8 complete
Breadth-first search | Direction-optimizing | 4 complete
Betweenness centrality | Brandes | 4 complete
Single-source shortest paths | Delta-stepping | 4 complete
Connected components | Afforest, Shiloach–Vishkin | 8 complete
Triangle counting | Ordered | 3 complete, 1 incomplete
Each implementation uses 4 inputs: Kronecker and uniform random graphs,
each at scales 16 and 22 with generator parameter k = 16.
Notes: Backup only. Every implementation has one profile for each of the four pilot inputs, for 32 profiles. Thirty-one are complete. Triangle counting on the larger Kronecker input timed out in its correctness verifier and remains incomplete. Its timing and simulation output must not be treated as correctness-verified performance. Existing implementations come from upstream GAPBS, including Jacobi.
Sources (repository snapshot a38dfac, reviewed 2026-09-24):
/Users/yanrujhou/CLionProjects/EvolveSWDB/records/kernels/
/Users/yanrujhou/CLionProjects/EvolveSWDB/records/implementations/
/Users/yanrujhou/CLionProjects/EvolveSWDB/records/inputs/
/Users/yanrujhou/CLionProjects/EvolveSWDB/records/profiles/

## Slide 8
Backup: implemented database operations
EvolveSWDB 2026-09-24 Backup
8
Capability | Implemented interface
Validate and store records | validate, add, build
Search access patterns and semantic facts | find, sql
Compare implementations of a kernel | implementations, including --applies
Screen strategy targets | strategies --pattern / --loop / --input
Export a workload view | view implementation input machine
Capture and profile the machine | capture-machine, profile
Refresh simulated cache metrics | recompute-cachegrind
Versioned YAML is the master copy. SQLite is generated for queries.
Notes: Backup only. YAML is the source of truth and SQLite is a generated query cache. Validation covers schemas, vocabularies and cross-record rules. Adding a record validates it before storing it and rebuilding the cache. Agent-origin additions retain draft status and agent-run provenance. Queries cover access patterns, semantic conditions, implementations and strategies. A workload view adapts stored records to the hardware-side format, but completed integration with a running HW agent is not established here.
Sources (repository snapshot a38dfac, reviewed 2026-09-24):
/Users/yanrujhou/CLionProjects/EvolveSWDB/swdb/cli.py
/Users/yanrujhou/CLionProjects/EvolveSWDB/swdb/db.py
/Users/yanrujhou/CLionProjects/EvolveSWDB/swdb/writer.py
/Users/yanrujhou/CLionProjects/EvolveSWDB/swdb/view.py
/Users/yanrujhou/CLionProjects/EvolveSWDB/docs/database.md
/Users/yanrujhou/CLionProjects/EvolveSWDB/docs/adr/0002-yaml-in-git-is-the-master-copy-sqlite-is-generated.md

## Slide 9
Backup: profiling and evidence types
EvolveSWDB 2026-09-24 Backup
9
Evidence | Recorded content | Interpretation
Correctness | Verifier outcome and timeout | 31 complete profiles
Timing | 1, 2, 4, 8, 16 threads, 5 trials | Measured application trial time
Memory footprint | Array sizes and footprint/L3 | Recorded sizes and formulas
Index stream | Reuse, sequentiality, degree skew | Features in 12 profiles
Cachegrind | Kernel-function cache references/misses | Simulated, single-threaded
Bottleneck | Classification with its basis | Inferred, not a counter measurement
Profiles retain source/build identity, commands, raw-output locations,
host load, thread binding, stage outcomes, and evidence references.
Notes: Backup only. The profiling pipeline records build provenance, host conditions, correctness checks and stages. Timing uses the application’s trial timer and retains all repetitions, medians, minima, maxima and spreads. Footprints use sizes and formulas. Index-stream features characterize recorded indirect streams and are available in 12 profiles, not all 32. Cachegrind simulates cache behavior at one thread, with kernel-function filtering. Bottleneck labels are inferences from counter-free evidence. The profile stores which stage completed and why other stages did not.
Sources (repository snapshot a38dfac, reviewed 2026-09-24):
/Users/yanrujhou/CLionProjects/EvolveSWDB/swdb/profile.py
/Users/yanrujhou/CLionProjects/EvolveSWDB/tools/index_features/
/Users/yanrujhou/CLionProjects/EvolveSWDB/docs/mbit10-profiling.md
/Users/yanrujhou/CLionProjects/EvolveSWDB/records/profiles/

## Slide 10
Backup: optimization strategies and intrinsics
EvolveSWDB 2026-09-24 Backup
10
Strategy | Target | Recorded effect
Packing | Access pattern | Indirect read becomes a stream, plus a packing pass
Software prefetch | Access pattern | Add a non-binding early access
SIMD gather | Access pattern | Widen lanes per access
Vertex reordering | Input | Reorder indices
Loop tiling | Loop | Restructure the loop
Intrinsic records: _mm_prefetch and _mm512_i32gather_ps
Strategy application links and derived ISA checks are implemented.
Notes: Backup only. The five strategy records identify changes by target and effect rather than name alone. Parameters such as distance or tile size do not create a new strategy identity. Preconditions return legal, illegal or undetermined, with unencoded obligations retained as manual checks. Benefits in strategy records are reported claims, not measured gains in this project. The intrinsic records cover the prefetch wrapper and an AVX-512 gather wrapper. Intrinsic use derives required ISA extensions for an implementation.
Sources (repository snapshot a38dfac, reviewed 2026-09-24):
/Users/yanrujhou/CLionProjects/EvolveSWDB/docs/adr/0004-optimization-strategy-is-a-record-identified-by-its-effect.md
/Users/yanrujhou/CLionProjects/EvolveSWDB/records/strategies/
/Users/yanrujhou/CLionProjects/EvolveSWDB/records/intrinsics/
/Users/yanrujhou/CLionProjects/EvolveSWDB/swdb/strategy.py
/Users/yanrujhou/CLionProjects/EvolveSWDB/swdb/isa.py

## Slide 11
Backup: safeguards and remaining boundaries
EvolveSWDB 2026-09-24 Backup
11
Implemented safeguard | Remaining boundary
Schema, vocabulary, cross-record checks | Valid structure does not establish a research claim
Unknown semantics remain unknown | Strategy screening is not a full correctness proof
Derived ISA and compiler/machine checks | No strategy-applied implementation measured yet
Correctness status and incomplete profiles | Triangle counting / large Kronecker is incomplete
Evidence basis and raw-output references | Simulated cache misses and inferred bottlenecks
Workload-view generation | Live HW-agent integration not demonstrated
Measurement context: shared mbit10 host, one socket per run.
This update uses committed profile records, not a new measurement campaign.
Notes: Backup only. These distinctions prevent a schema-valid record from being mistaken for a scientifically established result. The database checks references and evidence bases, preserves unknown semantics and enforces ISA requirements during profiling. Workload view generation exists, but this deck does not assert completed hardware-agent integration. The shared-host measurements are from committed profile records. This deck preparation did not rerun them or independently recheck the remote raw files.
Sources (repository snapshot a38dfac, reviewed 2026-09-24):
/Users/yanrujhou/CLionProjects/EvolveSWDB/swdb/rules.py
/Users/yanrujhou/CLionProjects/EvolveSWDB/swdb/validate.py
/Users/yanrujhou/CLionProjects/EvolveSWDB/swdb/isa.py
/Users/yanrujhou/CLionProjects/EvolveSWDB/swdb/profile.py
/Users/yanrujhou/CLionProjects/EvolveSWDB/swdb/view.py
/Users/yanrujhou/CLionProjects/EvolveSWDB/.claude/rules/remote_server.md

## Slide 12
Backup: PageRank timing and setup
EvolveSWDB 2026-09-24 Backup
12
Intel Xeon Gold 6326, one socket, 24 MiB L3, 5 trials at each thread count
Threads | Scale 16 median (ms) | Scale 22 median (ms)
1 | 20.45 | 2539.72
2 | 10.28 | 1281.29
4 | 5.28 | 646.16
8 | 5.18 | 335.84
16 | 5.20 | 190.22
Scale 16: 65,536 vertices, recorded footprint 8.33 MB
Scale 22: 4,194,302 vertices, recorded footprint 580.35 MB
Timing scope: application Trial Time. Raw runs date to 2026-09-22.
Notes: Backup only. These are medians in milliseconds, rounded from the profile records. Speedup is the one-thread median divided by the 16-thread median. Each median uses five trials. The two experiments have different graph sizes, so absolute times should not be compared as a speedup. The footprint is recorded in decimal MB, and the cache is 24 MiB = 25,165,824 bytes. The labels parallelism_bound and memory_bound are stored inferences. The small-input implementation uses dynamic scheduling with a chunk size of 16,384. Timing is the application Trial Time, not end-to-end process wall time. Raw records identify build commits and raw-output paths. This deck does not independently revalidate remote files.
Sources (repository snapshot a38dfac, reviewed 2026-09-24):
/Users/yanrujhou/CLionProjects/EvolveSWDB/records/profiles/gapbs-pr-jacobi.kron-g16-k16.mbit10.20260922t212416z.yaml
/Users/yanrujhou/CLionProjects/EvolveSWDB/records/profiles/gapbs-pr-jacobi.kron-g22-k16.mbit10.20260922t215412z.yaml
/Users/yanrujhou/CLionProjects/EvolveSWDB/apps/gapbs/src/pr_spmv.cc
/Users/yanrujhou/CLionProjects/EvolveSWDB/records/machines/mbit10.yaml