## Slide 1
EvolveSWDB weekly update
From a software database to evaluating BFS rewrites
Yan-Ru Jhou 2026-09-30
1
Notes: 0:00–0:20. Title. This week covers 2026-09-23 to 2026-09-29.

## Slide 2
Where we are
EvolveSWDB 2026-09-30
2
Last week
Built the Software Database
• Real code + memory access patterns
• Inputs, machine, measured profiles
• Query and export for the agents
This week
Use it to evaluate code rewrites
• Agent proposes a change to BFS
• We build, check, and measure it
• Native CPU and DX100 simulation
Question: can a rewrite proposal go from bottleneck to a trustworthy result?
Notes: 0:20–1:20 (60 s). Last week we built the Software Database: records of real code, memory access patterns, inputs, machines, and profiles, with query and export interfaces. It stored knowledge but could not yet act on it. This week's question: can an agent's rewrite proposal be carried all the way from a measured bottleneck to a trustworthy result? We chose BFS as the first complete case, because it has two very different starting implementations: upstream GAPBS direction-optimizing BFS, and the scalar top-down BFS from the DX100 accelerator paper, which also lets us target an accelerator.
Sources:
weeklogs/2026-09-24/speaker-notes.md
.scratch/bfs-rewrite-evaluation-2026-09-25/spec.md

## Slide 3
Why an evaluation workflow?
EvolveSWDB 2026-09-30
3
 | What it means for us
Motivation | Agents will propose rewrites; each needs a trustworthy verdict
Problem | Guesses and aggregate counters do not locate a workload’s hot code
Problem | Two BFS origins: speedup is ambiguous without an explicit baseline
Solution | One workflow: profile → propose → apply → check → measure → store
Stand-in | Representative proposals until the live agents are ready
Failures and regressions are kept too, not only wins.
Notes: 1:20–2:30 (70 s). Motivation: the SW and HW ensemble agents, being built by Peter and Josh, will propose rewrites. A proposal is only useful if someone independently applies it, checks it is still correct, and measures it on the exact workload. Problem: source-level guesses and whole-program counters do not tell us where a specific BFS run spends time, and two BFS versions from different origins cannot be compared without a stated baseline. Solution: one public interface that profiles, accepts a proposal, applies it, checks correctness, measures, and stores everything, including failures. Since the live agents are not ready, we use representative proposals that exercise the same real path.
Sources:
.scratch/bfs-rewrite-evaluation-2026-09-25/spec.md

## Slide 4
The workflow on one example
EvolveSWDB 2026-09-30
4
Profile
Propose
Apply
Check
Measure
Store
Find hot loop
+ memory behavior
Patch: 64-vertex
chunks, drop
redundant store
Build candidate
from exact source
BFS tree valid
on every trial
Paired timing
vs. baseline
Result kept,
incl. failures
Two proposal forms
Instructions: natural language or structured steps
Code: a patch or annotated source
The system never picks its own optimization; it evaluates the one proposed.
Notes: 2:30–3:50 (80 s). Here is the path with a real example. Profiling finds the hot BFS loop and its memory behavior. The proposal here is a patch for the DX100 scalar BFS: process vertices in chunks of 64 and drop a redundant store after an atomic compare-and-swap. The system applies the patch to an identified source snapshot, compiles it, checks the BFS tree on every timed trial, and measures only the declared region of interest against the unmodified baseline, in paired runs. Everything is stored and retrievable later from a fresh process. Proposals can arrive in two forms: instructions, in natural language or structured, and code, as a patch or annotated source.
Sources:
.scratch/bfs-rewrite-evaluation-2026-09-25/issues/18-dx100-patch-route-acceptance.md
.scratch/bfs-rewrite-evaluation-2026-09-25/spec.md

## Slide 5
What we have done this week
EvolveSWDB 2026-09-30
5
Area | Status
Workflow interfaces (profile, apply, check, measure, store) | Done
DX100 build, correctness, profiling support | Done
Native runs: DX100 patch route, upstream instruction route | Done
Remaining routes and DX100 simulation runs | In progress
Final coverage report and handoff | In progress
2 implementations × 2 proposal forms × 2 graph families = 8 cases
Acceptance: 11 of 20 criteria met. Test suite: 2,672 passed, 0 failed.
Notes: 3:50–5:00 (70 s). The first deliverable covers two starting implementations, two proposal forms, and two graph families, Kronecker and uniform random: eight cases. All workflow interfaces are implemented: profiling hot functions and loops, memory observations, rewrite application with bounded repair, native evaluation, DX100 build, correctness, and profiling. The native CPU cases for one route on each implementation ran end to end on the lab host. The remaining cases need the DX100 simulator or new proposals and are in progress. The acceptance report currently shows 11 of 20 criteria met. The full test suite passed: 2,672 tests, 0 failures.
Sources:
.scratch/bfs-rewrite-evaluation-2026-09-25/map.md
.scratch/bfs-rewrite-evaluation-2026-09-25/issues/21-coverage-roi-gain-and-handoff.md

## Slide 6
First native results: no measurable change
EvolveSWDB 2026-09-30
6
mbit10 Xeon Gold 6326, 1 thread, 10 paired repetitions, BFS region only
Proposal | Graph | Baseline (ms) | Candidate (ms) | Speedup | 95% CI
DX100 BFS: patch | Uniform | 46.03 | 45.96 | 1.002 | [0.998, 1.011]
DX100 BFS: patch | Kronecker | 23.26 | 23.23 | 1.000 | [0.996, 1.020]
GAPBS BFS: instructions | Uniform | 7.33 | 7.29 | 1.002 | [0.999, 1.005]
GAPBS BFS: instructions | Kronecker | 6.00 | 5.99 | 1.001 | [0.999, 1.030]
Correct on all timed trials. Spread above the 10% limit, so the verdict is “inconclusive”.
Small edits, no gain. The workflow refuses to report noise as a speedup.
Notes: 5:00–6:30 (90 s). Setup: mbit10, Intel Xeon Gold 6326, one socket, one thread. Ten paired repetitions per graph, baseline and candidate alternating, timing only the BFS region. The protocol requires a speedup of at least 1.05 and a run-to-run spread under 10 percent to call a result. Result: both proposals changed real code and passed correctness on all 30 timed trials per role. Speedups are 1.000 to 1.002, and every 95 percent interval includes 1. Spread was above the 10 percent ceiling, so the verdict is inconclusive. Analysis: these were small edits, a chunk-size change and removing dead work, so no gain is expected; the value is that the pipeline gives a conservative verdict instead of reporting noise as a win.
Sources:
.scratch/bfs-rewrite-evaluation-2026-09-25/issues/18-dx100-patch-route-acceptance.md
.scratch/bfs-rewrite-evaluation-2026-09-25/issues/19-upstream-instruction-route-acceptance.md

## Slide 7
Ongoing work and what we learned
EvolveSWDB 2026-09-30
7
Challenge | What we did | Status
LLM proposals: timeouts, one bad patch | Added whole-file edit format | New candidate built next
DX100 simulations take hours | Parallel runs within one socket | Running
Shared host: 2 jobs max | Queue per socket lane | Ongoing
Harness overhead per trial | Cached record parsing: 8.7 s → 1.0 s | Fixed
Lesson: most of the cost is around the experiment, not in it.
Notes: 6:30–8:00 (90 s). Three things slowed us this week. First, getting a proposal from the language-model provider: several attempts timed out, and one returned a patch that did not apply. We added a whole-file edit format, and it produced a candidate that now waits for a build. Second, the DX100 reference and control runs are simulations that take hours; gem5 is single-threaded and deterministic, so we now run several simulations inside one socket lane and plan one replay per source if replays show identical ticks. Third, the shared lab host allows two jobs at once, one per socket, and one socket is often held by another project. We also sped up our harness: a per-trial save fell from 8.7 to 1.0 seconds.
Sources:
.scratch/bfs-rewrite-evaluation-2026-09-25/issues/20-upstream-annotated-route-acceptance.md
.scratch/bfs-rewrite-evaluation-2026-09-25/resume-plan-20260927.md
.scratch/bfs-rewrite-evaluation-2026-09-25/issues/18-dx100-patch-route-acceptance.md

## Slide 8
Plan for this week
EvolveSWDB 2026-09-30
8
1
Finish DX100 reference and control simulations
Explicit baseline for accelerated results
2
Evaluate remaining routes, incl. DX100 candidates
All 8 cases covered
3
Coverage report + handoff to SW/HW ensembles
Agents use the workflow directly
Next question: do larger rewrites give measurable gains?
Notes: 8:00–9:30 (90 s). This week we will finish the first deliverable. One: freeze the simulator protocol and complete the DX100 reference and control runs, so accelerated results have an explicit unaccelerated comparison. Two: evaluate the remaining proposal routes, including at least one candidate that uses DX100 from each starting implementation. Three: generate the coverage report across all eight cases and hand the interface to Peter's SW ensemble and Josh's HW ensemble. Then the next question becomes whether proposals that are larger than these small edits produce measurable gains.
Sources:
.scratch/bfs-rewrite-evaluation-2026-09-25/spec.md
.scratch/bfs-rewrite-evaluation-2026-09-25/map.md

## Slide 9
Backup: native measurement protocol
EvolveSWDB 2026-09-30 Backup
9
Setting | Value
Host | mbit10, Intel Xeon Gold 6326, one socket lane
Threads | 1
Repetitions | 10 paired (baseline / candidate alternating)
Claim rule | Speedup ≥ 1.05 and spread ≤ 10%
Correctness | BFS tree checked on every timed trial
Profiling | Region timers + Callgrind (no HW counters)
Notes: Backup. The native protocol was frozen from a one-thread pilot study. Baseline and candidate trials alternate in pairs to reduce drift on a shared host. Correctness is verified outside the timed region. A speedup is claimed only if the lower confidence bound exceeds 1 and the minimum speedup and spread rules pass. The host load is recorded with every run. No hardware counters are available to our account, so profiling uses region timers and Callgrind memory simulation.
Sources:
.scratch/bfs-rewrite-evaluation-2026-09-25/issues/18-dx100-patch-route-acceptance.md
.claude/rules/remote_server.md